## Slide 1: HERON Workshop Examples
A case-by-case training in running HERON
INL/MIS-22-65661

## Slide 2: Learning by Example
HERON cases from basic to complex
Exercises, follow-alongs
Examples found in HERON/tests/workshop/htse
TODO

## Slide 3: Example 1
As Simple As They Come

## Slide 4: Starter Case
Components
  NGCC (natural gas electricity generator)
  Import (imports electricity from external)
  Grid (demand to be met)
Objective
  How big should the NGCC be built to minimize costs?

## Slide 5: Starter Case
Guiding Physics/Economics (Drivers)
  Grid
    fixed demand to be met
  NGCC
    Capital cost for sizing
    Variable cost for dispatching
  Import
    Variable cost (expensive!) for providing electricity

## Slide 6: Translating to HERON
See HERON/tests/workshop/htse/example1_simple/heron_input.xml
Case
  Global information about the problem
  Time shape, discount rates, solvers, etc.
Components
  Technical and economic properties of each component
  Produces and Demands
  Dispatch: Independent and Fixed
DataGenerators
  Synthetic History Data Source

## Slide 7: Component by Component
Grid
  Technical Specs
    Demands electricity
    Fixed dispatch (no flexibility, demand must be met)
    “Capacity” (demand) depends on synthetic time series
      Note: time series generators trained separately
  Economics
    None
      Regulated market example
      Minimize cost to meet demand

## Slide 8: Component by Component
NGCC
  Technical Specs
    Produces electricity
    Independent dispatch (0 to Capacity each hour)
    Capacity (electricity) optimized from 10 GW to 40 GW
      Note: units (GW) are up to the user but should be consistent!
  Economics
    Capex, driven by capacity
    Variable O&M, driven by activity
      Cost of natural gas, etc
Talk about ValuedParams, Fixed Value
Depreciation, DiscountRate
resource conventions

## Slide 9: Component by Component
Import
  Technical Specs
    Produces electricity
    Independent dispatch (0 to Capacity each time step)
    Capacity (electricity) fixed at large number
      Note: consider demand to know what fixed cap is enough!
  Economics
    Variable O&M, driven by activity
      Cost of importing electricity

## Slide 10: Consider the Case
Why Import?
  Why not just have NGCC?
  If NGCC not enough to meet demand, solve “fails”
    This doesn’t provide useful feedback to optimizer; it doesn’t know what’s wrong
    Instead, provide large incentive to meet demand with NGCC
    Example:
GW
NGCC
Import
Demand

## Slide 11: Demand
Stochastically Trained
Based on NYISO projections from EPRI
See INL/EXT-21-65473,
“A Technical and Economic Assessment of LWR Flexible Operation for Generation/Demand Balancing to Optimize Plant Revenue”, Dec 2021

## Slide 12: Running the Case
Check Parallelization
  Available threads: cpus * cores/cpu * threads/core
    search: how many threads does my computer have [windows/mac/linux]
    useful parallelization -> limited by inner, outer characteristics
/path/to/heron heron_input.xml + outer
It’s optimizing, so it will take a bit!
Things to look at (see following slides):
  1_simple_o/opt_soln_0.csv (spreadsheet) optimizer progress
  Screen Output

## Slide 13: Things to Look At While Running
1_simple_o/opt_soln_0.csv – progress of the optimizer
case name
outer
optimization record
Optimizer Steps
(sets of samples)
Status of each step
Accepted: improvement!
Rejected: went too far
Rerun: re-check gradient
Component Sizes
(opt variables)
Mean NPV
(objective)
Note our losses are getting smaller!

## Slide 14: Things to Look At While Running
Screen Output: How To Read the Matrix
  Accepted Sample
    This means a new optimal point has been found!

## Slide 15: Things to Look At While Running
Screen Output: How To Read the Matrix
  Rejected Sample
    This means the new proposed opt point is worse than the old opt point
    Reasons: inaccurate gradient, too large step, no better points nearby
    Happens frequently, especially near the end

## Slide 16: Things to Look At While Running
Screen Output: How To Read the Matrix
  Rerun Sample
    Return to best-so-far opt point and rerun the gradient, cut step size
    Helps to resolve two reasons for rejecting proposed opt points

## Slide 17: Now that it’s done …
Things to look at (see next slides)
opt_soln_0.csv
  filter opt CSV by “accepted” to see acceptance path
  final solution is the last “accepted” point in the CSV
opt_path.png
  visualization of opt_soln_0.csv
screen output

## Slide 18: Things to look at now that it’s done
Screen Output
Summary of optimizer status
  Trajectory that found best point
  Objective value
  Opt Vars values
opt var
objective
isn’t 40 GW kind of insane?

## Slide 19: Things to look at now that it’s done
1_simple_o/opt_soln_0.csv
Last “accepted” point is solution
  200 iterations is low (good!)
  Sort by “accepted” then “iteration”
opt var
objective

## Slide 20: Things to look at now that it’s done
1_simple_o/opt_path.png
Messy plot
Many plots are bad
    but some are useful
Not intended for report quality
  Indicative of process
capacities
(opt vars)
towards the end only small changes
E[NPV]
(objective)
most optimization happens in the first
few time steps

## Slide 21: Wrap up Example 1
That’s it!
Takeaways:
  3-unit problem, single resource
  Setting up feasible problems
  Running and observing HERON runs
  Viewing results

## Slide 22
TODO other examples
  Add battery storage
  multi-resource (HTSE, hydrogen market)
  VREs (wind, solar)
  technical complexity
    transfer functions
  economic complexity
    Multiple markets
    regulated vs deregulated
    price taker, price maker
Synthetic Histories
Gathering input data
  demand, vre
  WACC, economic factors
  technical properties of components